## Slide 1: ESP32 Dev Module V4
IoT Project

## Slide 2: Hardware Layout

## Slide 3: Hardware Detail
LCD display with HD44780 driver
+5V
+3.3V
GND
PCB Top
PCB Bottom
LED1
LED2
BUT1
BUT2
Photo-resistor
Avoidance
Temperature &
Humidity

## Slide 4: ESP32 Module Pinout

## Slide 5: Hardware Configuration
GND
+5V
SDA
SCL
GPIO13
GND
EN
GPIO17
10K
10K
910
910
+3.3V
+3.3V
+5V
+3.3V
GPIO12
GPIO2
GPIO14
GPIO16
GPIO5
GPIO4
GPIO22
GPIO21
GND
Avoidance
Temperature &
Humidity
Photo-
resistance
LED1
LED2
BUT1
BUT2

## Slide 6: Configuration Table
Sensor/Device | Interface | Remark
LCD Panel | SDA=GPIO21 SCL=GPIO22 | 16 x 2 Characters LCD module
Button1 (BUT1) | GPIO17 (Internal pull-down) | Push to high
Button2 (BUT2) | GPIO16 (Internal pull-down) | Push to high
LED Red (LED1) | GPIO5 | High to turn-on
LED Green (LED2) | GPIO4 | High to turn-on
Avoidance | Enable=GPIO14 Output=GPIO15 | Output=L  Obstacle Output=H  No obstacle
Temperature & Humidity | Data=D1 | Digital output of T and H values
Photo-resistance | Output=GPIO13 | Darkness: ~50kΩ Light: ~500Ω

## Slide 7: Project scopes
Temperature and humidity measure and read at LCD display.
Flash LED Red (LED1) for every sample of captioned parameters.
Button 1 (BUT1) toggle to measure parameters of Avoidance and Photo-resistor.
Flash LED Green (LED2) for every sample of captioned parameters
Button 2 (BUT1) to try to enable/disable to WIFI connection to connect cloud base system.
If connected good, turn on LED2.
Cloud will collect all four sensor parameters: Temperature, humidity, avoidance and photo-resistor.